## Slide 1: Operating System
Chapter 1-2: Basic Concept and Prerequisite knowledge
宫晓利
Department of Computer Science, NanKai University
Email: gongxiaoli@nankai.edu.cn

## Slide 2: Computer Hardware Review
Processors: Architecture and Modes
Memory: Hierarchy of storage systems
I/O Devices: Clock, keyboard, monitor and hard disk
Buses: Organization of computer system

## Slide 3: History of Processors
The beginning of microprocessor
  1960s, Intel 4004 & Intel 440
  4bits, 4K address space, 45 instructions, 50KIPS
The beginning of modern microprocessor
  1971, Intel 8008: 8bits, 16K address space, 48 instructions, 50KIPS
  1973, Intel 8080 & 8085: 64K address space, ,246 instructions, 500KIPS
  1973, Motorola MC6800; Zilog Z80; MOS 6502
16 bit microprocessor
  1978, Intel 8086; 1979, Intel 8088; 1983, Intel 80286
  16bits, 1MB address space, 20K instructions, 2.5MIPS & 4.0MIPS
  Motorola MC68000
32 bit & 64 bit microprocessor
  Intel 80386(1986), Intel 80486(1989), Intel Pentium(1993)
  32bits, 4GB address space, CISC & RISC, xGIPS
  64bits, 64PB address space,

## Slide 4: Guide line of processor’s capability
Frequency
  CPU clock speed = CPU socket speed * clock multiplier
  CPU socket speed: the times per second that transfer data from/to CPU, generated by mainboard
  Front side bus speed: the bandwidth that transfer data between “Northbridge” chip and CPU
  Clock multiplier
  Memory clock speed
Instruction set & Coprocessor
  CISC, RISC
  Float processor, Boolean processor
Cache
  Level1& Level 2 cache: registers & buffers
Architecture
  Micro-architecture, Superscalar & super-pipeline
Technics
  45nm32nm22nm14nm5nm

## Slide 5: How CPU evolves
CPU DB: Recording Microprocessor History, Danowitz et al. Communications of the ACM, Vol. 55 No. 4, 2012.

## Slide 6: Structure of microprocessor
Execute unit
  Execute the specified instruction
Control unit
  Fetch instruction from memory to registers
  Maintain the status of CPU
  Data transfer between CPU and memory
Register and Cache
Pipeline && Parallize

## Slide 7: Instruction cycle of processor
Fetch instruction from memory
  Program Counter stores the address of next instruction
  Processor fetch the instruction via memory access
Decode instruction
  Store the parameters of the instruction into registers
Execute instruction
  Instruction Register stores current instructions
  Integer, float and Boolean processors
Pipeline
  Sequence of circuit units to execute an instruction
Start
Fetch unit
Decode unit
Execute unit
End

## Slide 8: Registers in CPU
Address register
  Store the address of data or instruction
Data register
  Store the operand/operator of instruction
Flag register
  Store the flags of operation
Control and status register
  Used by OS for managing CPU
Operating System
CITS, NanKai University
8

## Slide 9: Registers in CPU (privileged)
Program counter
  The register that stores address of next instruction
  Each process has its private PC value
Instruction register
  Stores the instruction to be executed
  Each process has its private IC value
Program status word
  The register that stores flags and conditions of CPU working status
  PSW is the most important part of CPU context
Operating System
CITS, NanKai University
9

## Slide 10: PSW of Intel CPU
Operating System
CITS, NanKai University
10
CF： 进位标志位
ZF： 结果为零标志位
SF： 符号标志位
OF： 溢出标志位
标准条件位：
TF：陷阱标志位
IF：中断允许（中断屏蔽）标志位
VIF：虚拟中断标志位
VIP：虚拟中断待决标志位
IOPL：IO特权级别

## Slide 11: PSW的使用示例
Load AX 0xfffffff1
ADD AX 0x5F
Load AX 0x0
ADD AX 0x50
Operating System
CITS, NanKai University
11
这两段指令执行之后，AX寄存器的值一样吗？
他们发生的事情一样吗？
如何知道这些差异？

## Slide 12: Essential of CPU
Rank of CPU instruction
  R0: privileged instruction only used by OS
  R1: important device driver and I/O routine
  R2: protected program, such as IDE
  R3: user space for common program
Working mode of CPU
  Kernel mode & User mode
“Trap”
  Switch the mode of CPU from “user” mode to “kernel” mode
Operating System
CITS, NanKai University
12

## Slide 13: Computer Hardware Review
Processors: Architecture and Modes
Memory: Hierarchy of storage systems
I/O Devices: Clock, keyboard, monitor and hard disk
Buses: Organization of computer system
Operating System
CITS, NanKai University
13

## Slide 14: Storage system in computer
Operating System
CITS, NanKai University
14

## Slide 15: 一些非常重要的数字
By Jeff Dean: http://research.google.com/people/jeff/

## Slide 16: Strategy of storage system
Guide lines for storage system
  Speed: should be not slower than CPU speed
  Size: should be enough large that can store everything
  Cost: should not be expensive for most customers
Strategy for a reasonable storage system
  Local optimal principle
  Hierarchy architecture
Various kinds of memory
  Register, RAM, SRAM, DRAM, SDRAM, DDR
  ROM, PROM, EPROM, EEPROM, CMOS
  Flash memory
Operating System
CITS, NanKai University
16

## Slide 17: Local optimal principle
A story about Yangguo and Xiaolongnv
  The answer exists around the question
Local optimal principle in address space
  The address of next instruction should be adjacent to current instruction
Local optimal principle in time sequence
  The instruction used recently should be used again in the near future
Principle of Cache design
  Only stores the instructions that belong to a local region, both in address space and time sequence
  Small size, but higher performance and cheap price
Operating System
CITS, NanKai University
17

## Slide 18: Local optimal principle
Operating System
CITS, NanKai University
18

## Slide 19: Memory Management
19
在多道环境中存储管理要解决的主要问题是：
用户程序间如何保护
核心程序如何受到保护
执行程序如何重定位

## Slide 20: Memory Management
20
One base-limit pair and two base-limit pairs
硬件提供基址和界限寄存器为内存管理提供基础：

## Slide 21: Computer Hardware Review
Processors: Architecture and Modes
Memory: Hierarchy of storage systems
I/O Devices: Clock, keyboard, monitor and hard disk
Buses: Organization of computer system
Operating System
CITS, NanKai University
21

## Slide 22: Clock in computer
What dose time means in computer
  The speed of operation and execution
  The criterion of resource management
  The bandwidth of data transfer
  The record of real time
Components of programmable clock
  Crystal oscillator: physical component
  Counter: decremented at each pulse
  Holding register: record the initial value of counter
One-shot clock and square-wave clock
  One-shot clock: controlled by OS software
  Square-wave clock: generate periodic signal
  Clock tick: periodic interrupts
Operating System
CITS, NanKai University
22

## Slide 23: Clock and clock interrupts
Operating System
CITS, NanKai University
23
每个脉冲使计数器减1，归零则产生时钟中断
用来装入计数器初值

## Slide 24: Essential of Interruption
Operating System
CITS, NanKai University
24

## Slide 25: Essential of Interruption
Operating System
CITS, NanKai University
25
开始
取下一条指令
执行指令
检查指令
处理中断
停止
取周期
执行周期
中断周期
不允许中断
允许
中断

## Slide 26: Essential of Interruption (unnested)
Operating System
CITS, NanKai University
26

## Slide 27: Essential of Interruption (nested)
Operating System
CITS, NanKai University
27
低优先级中断嵌套高优先级中断的处理流程

## Slide 28: Essential of Interruption
Operating System
CITS, NanKai University
28

## Slide 29: Interrupt, Exception and trap
Exception
  Errors found by hardware, caused by program
  Divide by 0, floating-point underflow, access denied
  The exception will be handled by OS in kernel mode, or informed to the program and handled by user program
Interrupt
  Signal sent from hardware to CPU
  CPU finds and invokes interrupt handler (kernel mode)
  In time-sharing OS, the interrupts are handled in clock interrupt function
System call
  Interface provided by OS to allow programs obtaining some system service
  “Trap” instruction will trap into kernel mode and invoked OS to execute service
Operating System
CITS, NanKai University
29

## Slide 30
Operating System
CITS, NanKai University
30

## Slide 31: I/O Device
31
I/O模块由一些设备控制器和相应的软件构成
  处理器与I/O模块交互方式：
  专用指令完成I/O访问
    指令格式不变，对存储器访问换成I/O模块访问
  I/O模块与存储器间交互 ：用 DMA（Direct Memory Access)模式

## Slide 32: I/O Communication Techniques
32
1）程序控制I/O方式
由I/O软件控制I/O操作，包括设备状态检测、发送读写命令和传送数据等，无中断。
2）中断驱动I/O方式
处理器发传送命令后，转去做其他的工作，I/O准备好后打断处理器的工作，完成数据传递。
3）直接存取I/O方式
外设与内存直接存取，处理器只参与数据传递中的头尾过程。

## Slide 33: I/O Communication Techniques
33
(a) 启动I/O设备并引发中断的步骤
(b) CPU 是如何完成中断处理的
(a)
(b)

## Slide 34: Tape is Dead Disk is Tape Flash is Disk RAM Locality is King
Jim Gray
Microsoft
December 2006

## Slide 35: Computer Hardware Review
Processors: Architecture and Modes
Memory: Hierarchy of storage systems
I/O Devices: Clock, keyboard, monitor and hard disk
Buses: Organization of computer system
Operating System
CITS, NanKai University
35

## Slide 36: Architecture of Computer
Operating System
CITS, NanKai University
36

## Slide 37: North bridge and south bridge
North bridge
  Transfer data between CPU and memory/AGP
  More expensive, faster and complicated
South bridge
  Transfer data between I/O buses and devices
  Cheap, slow and cheap
The communication between I/O and CPU
  CPU don’t access I/O device directly
  Some special mechanisms are designed for the link between north bridge and south bridge (DMA, I/O channel)
  Intel Hub Architecture, SIS Multithread(妙渠)
Operating System
CITS, NanKai University
37

## Slide 38: 你需要记住的硬件细节
CPU是没有状态的，寄存器和内存代表了CPU的状态
高速存储永远都不够用，所以只能用局部性原理“欺骗”程序员
指令是不可以被打断的，中断只在指令之后处理，异常会在指令之前处理

## Slide 39: Thanks for your time! Questions & Answers